Setting up TSC - alpha with a Raspberry Pi 3 Model B
TSC (TwoStepperControl) is a software project by Wolfgang Birkfellner and Steffen Elste to realize an open integrated control system for astronomical telescopes. The basic idea is to use a Raspberry Pi to control a telescope and to provide basic autoguiding functionality without additional external computers. As Raspbian Jessie is not an RTOS, it cannot control stepper drivers directly like a microcontroller; therefore, extra hardware is necessary which receives basic parameters (number of steps, velocity, acceleration) from the software. Currently, I am using a Phidgets 1067 bipolar driver board although other alternatives are under consideration. The steppers are monitored by the Pi in separate Qt-Concurrent threads so that software functionality is maintained during stepper operation. So far, only fork mounts are supported.

Software repository:
https://github.com/selste/TwoStepperControl
Details on the software setup are covered in the Wiki on github – this Readme documents Raspian system setup measures and hardware required.

Installing TSC:
Get yourself a good quality 16 GB SD-card and copy an image of the Raspian running TSC. In Ubuntu, this is done by typing
dd if=/dev/tscimage.img of=/dev/mmcblk0 bs=8M

Basic components:
- Operating System: Raspbian Jessie - https://www.raspberrypi.org/downloads/noobs/
- Currently, the locale should be english.
- Raspberry Pi 3 Model B, with at least a 16 GB MicroSD card and a 2A micro-USB power adapter. Cost ~ 70 €. I would recommend connecting the Pi to the motor power supply while using a step-down converter.
- Be aware that one needs a lot of power to drive the Phidget boards. Get yourself a sufficient power supply for everything else but the Pi.
- Buy cooling bodies for the Pi, especially the ARM CPU (~5 €), and plan to get a fan for the Pi and the Phidget boards.
- Stepper control boards: Currently, 1067_0 - PhidgetStepper Bipolar HC, available from www.phidgets.com or www.nodna.de are used. Two boards are necessary. These operate one bipolar stepper each with up to 4 A coil current. 1/16 microsteps are available, the board is controlled via USB 2.0. Cost for each board is currently ~90 €. A development with alternate driver boards is under way but not yet available. As Raspian is not a RTOS, it cannot control the drivers directly.
- A Raspberry Pi compatible USB 2.0 hub with separate power. Not all hubs work, so be careful.
- An Adafruit DS3231 buffered clock module, so that the Pi also knows the proper time when being operated without internet connection: https://learn.adafruit.com/adding-a-real-time-clock-to-raspberry-pi/set-rtc-time?view=all
- ---------------------------------------------- Optional components -------------------------------------
- Optionally, a HDMI cable and an HDMI monitor. Development right now aims at using the Adafruit 5” HDMI 800*480 Backpack Touchscreen (~80 €). Basically, it is also possible to connect via W-LAN or WI-FI direct and a VNC viewer to the Raspberry using a mobile or a tablet – check the github Wiki for details. TSC is also configured to act as an independent hotspot, therefore this solution also works when no WLAN is available.
- Optionally, wireless mouse and keyboard. Cost ~20 €.
- Optionally, a RS232 adapter to connect to planetarium programs via wire. For this purpose, it is necessary to get a circuit like this one: https://www.conrad.at/de/rs232-erweiterungs-platine-fuer-den-raspberry-pi-1337093.html. Denote that this one needs a nullmodem-cable and a RS232 to USB converter if your computer does not have one. Alternatively, a direct CP2102 converter like this one might be of interest: https://electronics.semaf.at/navi.php?a=962&lang=eng. Denote that with certain programs like Sky Safari Plus and Cartes du Ciel, a TCP/IP connection is also possible. In this case, no converter is needed.
- For the optional bluetooth handbox, one also needs an Arduino Uno (24 € for the original one (strongly recommended) or a few coins for chinese copies - other models like the Nano might work as well) and a HC-05 bluetooth board (3-6 € + postage on ebay). Also, a lever switch and four touch switches, wires, a 9V power supply, a housing and 5 10k resistors are necessary. Putting the handbox on a prototype shield is feasible. An Arduino sketch can be found in the repository called “sketch_handbox_TSC.ino” for operating the handbox
- Software requirements:
  - Development environment is Qt and QtCreator using C++. Some info can be found – for instance on missing libxcb libraries- -here: https://wiki.qt.io/Native_Build_of_Qt_5.4.1_on_a_Raspberry_Pi
  - Install the Phidgets – library and set the right access privileges for the USB port if you don't want to run the program in root mode. Check
    http://www.instructables.com/id/Getting-Started-with-Phidgets-on-the-Raspberry-Pi/ …
    Basically, you need the libusb 1.0 and libphidgets 2.1. Changing the udev rules is also necessary (this is taken from http://tordwessman.blogspot.co.at/2012/01/running-phidgets-under-linuxubuntu.html):
    - $ sudo nano /etc/udev/rules.d/80_phidget.rules
    - Add the following content:
      SUBSYSTEMS=="usb", ACTION=="add", ATTRS{idVendor}=="06c2", ATTRS{idProduct}=="00[3-a][0-f]", MODE="666"
    - Set USB_DEVFS_PATH to /dev/bus/usb by adding to ~/.bashrc:
      export USB_DEVFS_PATH=/dev/bus/usb
    - Restart udev:
      $ services udev restart
    - If it doesn't work. Try the good old:
      $ sudo reboot
  - Image acquisition of guiding cameras is realized via INDI. A tutorial for installing it on the Pi is found under
    http://indilib.org/support/tutorials/139-indi-library-on-raspberry-pi.html
  - In order to utilize the serial port, one has to disable it's current purpose – serving as a console to the pi.
    - Edit /boot/config.txt by typing enable_uart=1.
    - Disable console output from Jessie by typing:
      $ sudo systemctl stop serial-getty@ttyS0.service
      $ sudo systemctl disable serial-getty@ttyS0.service
    - Type sudo nano /boot/cmdline.txt and remove the statement console=serial0,115200 from that text. After reboot, /dev/ttyS0 should be available. More can be found under
      http://spellfoundry.com/2016/05/29/configuring-gpio-serial-port-raspbian-jessie-including-pi-3/
    - Make the port readable for all: sudo chmod a+rw /dev/ttyS0
  - Enable the Autohotspot following the instructions from: http://www.raspberryconnect.com/network/item/315-rpi3-auto-wifi-hotspot-if-no-internet
  - Enable the hardware clock following the instructions from https://learn.adafruit.com/adding-a-real-time-clock-to-raspberry-pi/set-rtc-time?view=all

The Bluetooth handbox:
The handbox features five switches, one on/off switch for speed selection and four switches for motion. It features an Arduino Uno and a HC-05 Bluetooth interface. A simplified schematic is shown.

Setting up the HC-05:
- I follow the instructions from https://myraspberryandme.wordpress.com/2013/11/20/bluetooth-serial-communication-with-hc-05/
- For setup, the HC-05 “STATE” has to be connected to 5V. The sketch “sketch_HC05_setup.ino” is used to configure the HC-05. CR/LF have to be enabled for communicating via the serial interface.
- Send the following commands:
  - AT+NAME:TSC
  - AT+ADDR? gives the MAC address of the device – write it down!
  - AT+UART:9600,1,0 sets the communication parameters
  - AT+ROLE: 0 makes the device a slave
- Disconnect the wire from 5V to the STATE pin.

- Make sure that Bluez is downloaded - https://learn.adafruit.com/install-bluez-on-the-raspberry-pi/installation
- Write a file rfcomm.conf in /etc/bluetooth; it should read:
rfcomm0 {
# Automatically bind the device at startup
bind yes;
# Bluetooth address of the device
device 98:D3:31:FB:2A:8C
# your MAC address for the HC05 should go here!
# RFCOMM channel for the connection
channel 1;
# Description of the connection
comment "TSC";
}
- Write a file “pincodes” in “/var/lib/bluetooth/xx:xx:xx:xx:xx:xx/” where the PIN code of the HC05 is stored; this is usually 1234, it can be edited in setup, but this is default.
- Try to pair the HC05 by using the BT-tool … it should work now.

The ST 4 interface:
ST 4 can be used. For this purpose, a standard RJ 11 jack has to be wired to the GPIO port of the Raspberry Pi 3 as follows:
Direction	Direction	Wiring Pi Port	BCM Pin	Pi Pin	ST 4 Pin
Declination +	North	2	27	13	5
Declination -	South	4	23	16	4
Right Ascension +	West	5	24	18	3
Right Ascension -	East	3	22	15	6
GND				14	2

The ST 4 Pins, as seen from the jack. Numbering goes from right to left.	The GPIO pins of the Raspberry Pi3; the program needs the pins in the gray areas.